## Slide 1: Participatory Traffic Control with Connected and Automated Vehicles for Network Efficiency
Yafeng Yin, Ph.D.
Donald Cleveland Collegiate Professor of Engineering
Donald Malloure Department Chair of Civil and Environmental Engineering
University of Michigan, Ann Arbor
TRISTAN XII, Okinawa, Japan, June 22, 2025

## Slide 2: Contributors
Minghui Wu, Richard Lee, Xi Lin, and Jeff Scruggs, University of Michigan, Ann Arbor
Zhibin Chen, New York University Shanghai
Jerry Lynch, Duke University
Meng Li, Tsinghua University

## Slide 3: 1 Participatory Traffic Control 2 CAVs as Demand Distributors 3 Recruiting CAVs for Participation 4 Controlling CAVs for Network Efficiency 5 Concluding Remarks

## Slide 4: Participatory Traffic Control
Source: https://flow-project.github.io/
Utilizing connected and automated vehicles (CAVs) within the traffic stream as control actuators to manage traffic
CAVs as traffic stream regulator
  Wu et al. (2018), Stern et al. (2018) and Jin et al. (2018)
  “Flow control will be possible via a few mobile actuators (less than 5%)” (Stern et al., 2018)

## Slide 5: Leveraging Relinquished Human Agency in Travel
Human agency is the capacity for individuals to act independently and make their own decisions based on personal volition.
This concept is highly relevant to travel, encompassing multiple facets such as the timing of travel, choice of destination, mode, and route, driving tasks, and adaptability.
While traditionally personal vehicles have been marketed with cultural symbols of security, freedom, and control, the advent of driving automation requires travelers to increasingly surrender aspects of their agency.

## Slide 6: Leveraging Relinquished Human Agency
Human agency
Incentivized to relinquish
Enabled control
Destination
Mode
Departure time
Route
Driving maneuvers
Active travel demand management
CAVs as traffic demand distributors
CAVs as traffic stream regulators
Participatory Traffic Control

## Slide 7: CAVs as Traffic Demand Distributors
The working hypothesis is that, by controlling the departure time or route choice of a small number of CAVs, we can influence a larger number of uncontrolled vehicles’ travel decisions to improve the overall system performance.
What percentage of traffic do we need to control?
Let’s examine the minimum percentage of traffic that needs to be controlled to replicate system optimum in a traffic network

## Slide 8: Wardrop's Principles of Traffic Assignment*
* Wardrop J. (1952) Some Theoretical Aspects of Road Traffic Research. Proceedings, Institution of Civil Engineers II(1), pp. 325-378.
John Wardrop
(1922–1989)
Feature | First Principle (User Equilibrium) | Second Principle (System Optimum)
Behavior Type | Selfish (user optimal) | Altruistic or centrally controlled
Stability | Nash Equilibrium | Requires control to be stable
Realism | More realistic for decentralized systems | Ideal goal for planning or control
Total System Cost | Higher than or equal to SO | Minimal possible total travel time
Formulation |  | 

## Slide 9: Controlling CAVs to Replicate System Optimum
What is the minimum percentage of traffic that needs to be controlled?
  Cooperative AVs (CAVs): System optimum routing principle
  Uncontrolled Vehicles (UVs): User optimal routing principle
Braess network

## Slide 10: Minimum Control Ratio (MCR) Formulation
s.t. |  | (1)
 |  | (2)
 |  | (3)
 |  | (4)
 |  | (5)
 |  | (6)
 |  | (7)
 |  | (8)
 |  | (1)
 |  | (2)
 |  | (3)
 |  | (4)
 |  | (5)
 |  | (6)
 |  | (7)
 |  | (8)
  Set of paths with minimum travel time
Set of paths with minimum marginal travel time

## Slide 11: MCR in Real-World Networks*
Network | Zones | Nodes | Links | MCR (%)
Anaheim | 38 | 416 | 914 | 21
Barcelona | 110 | 1020 | 2522 | 36
Berlin-Mitte-Prenzlauer Berg-Friedrichshain-Center | 98 | 975 | 2184 | 14
Eastern-Massachusetts | 74 | 74 | 258 | 20
Sioux Falls | 24 | 24 | 76 | 14
Terrassa | 55 | 1609 | 3264 | 57
Winnipeg | 147 | 1052 | 2836 | 42
*Chen, Z., Lin, X, Yin, Y. and Li, M. (2020) Path controlling of automated vehicles for system optimum on transportation networks with heterogeneous traffic stream. Transportation Research Part C: Emerging Technologies, 110, 312-329.
Notes: 25%...

## Slide 12: Recruiting CAVs for Participation
Drivers delegating control to machines does not necessarily mean they are willing to sacrifice personal benefits for system-level improvements.
Incentives may be necessary to encourage CAV participation in traffic control schemes. These incentives should compensate drivers for their loss of agency and potential increases in travel costs.
So, how can we design effective incentive schemes to recruit CAVs for implementing participatory traffic control?

## Slide 13: Recruiting CAVs for Participation

## Slide 14: Morning Commute Setting (Vickrey, 1969)
William Vickrey
(1914-1996;
Nobel Laureate, 1996 )
Work starting time (9:30)
N persons
Capacity = s
Early/Late Arrival Penalty
Arrival Time

## Slide 15: Equilibrium Departure Time Choice
Travel Cost
Arrival Time
# of vehicles
Time
Queueing Diagram at Bottleneck
Cumulative arrivals at bottleneck
Cumulative departures at bottleneck
Total travel cost =

## Slide 16: Equilibrium vs Optimum
Optimum
Equilibrium

## Slide 17: Recruiting CAVs for Participatory Traffic Control
Group 1: Providing incentive in exchange for both departure time and maneuver control
recruited users
Heterogeneous cost of agency with PDF , CDF , and inverse CDF
Group 2: Providing incentive in exchange for driving maneuvers only
recruited users
Cost of agency with
Participatory Traffic Control
Departure time: placing Group 1 at the shoulders of the departure window
Maneuver: uniformly mixing Group 2 in the traffic stream with UVs
The bottleneck capacity 𝑠(𝑤) is an increasing function of the mixing rate of CAVs 𝑤 due to the smoothing effect. Denote , is the maximum capacity improvement ratio

## Slide 18: Equilibrium Solutions under Control
Cumulative departures/ arrivals
Time
Time
Travel cost
Group 1 CAVs
Group 2 CAVs
Average travel cost of Group 1 recruits
Equilibrium travel cost of remaining commuters

## Slide 19: First-Best Design
Total travel cost
Total cost of agency
Specification of and :
The smoothing effect is marginal increasing
Uniformly distributed
Capacity
Control rate
Operation cost

## Slide 20: Analytical Solutions
where , ,
.
Optimal incentives:
Conditions |  |  | 
Conditions |  |  | 
Unconstrained recruitment target for Group 1
Unconstrained total recruitment target
Adjusted recruitment target for Group 1 with Group 2 not being activated

## Slide 21: Managerial Insights – Economic Feasibility
The incentive scheme is always active if there exist drivers whose cost of agency is sufficiently small (e.g., the lower bound of the cost ) and the unit operation cost is sufficiently low compared to the equilibrium travel cost (
  No recruitment arises when . Since , these inequalities cannot hold simultaneously if both conditions are met
Empirical studies indicate that more than 60% of people are willing to take prosocial actions when there is no personal cost. This suggests a high likelihood of the existence of drivers with sufficiently low or zero agency costs.
Recruiting CAVs for participatory traffic control likely makes economic sense for rush hour congestion management.…

## Slide 22: Managerial Insights – Economic Feasibility
…. especially in large cities!
  The number of recruits increases as N increases
  In high-demand scenarios, travel cost dominates, and participatory control offers greater leverage to reduce the total cost
Total travel cost
Total cost of agency
Operation cost

## Slide 23: Managerial Insights – Hiring Strategy
We should generally prioritize recruiting Group 1, even though they are more costly to hire.
  This preference is driven by their marginally increasing smoothing effect and the presence of drivers with low agency costs.
  When , we always have Group 1 recruits. Positioning them at the shoulders, where the mixing rate is 100%, yields the greatest benefits.

## Slide 24: Managerial Insights – Hiring Strategy
The recruitment focus shifts toward Group 2 as the smoothing effect becomes stronger
  A higher leads to more recruits
  On the other hand, a higher 𝑟 leads to fewer recruits in Group 1, implying that the share of Group 1 in the recruits drops
  When 𝑟 increases, recruiting Group 2 becomes more cost-effective, as they are less costly but become more effective

## Slide 25: Numerical Validation
Scenarios |  | Smoothing effect |  | 
 |  | Marginal increasing | Linear | Marginal decreasing
Cost of agency | Uniform | (a) | (b) | (c)
 | Truncated normal | (d) | (e) | (f)
At and 10% AV market penetration, the recruitment level stays above 2% across all cases when varying 𝐷 and 𝑟

## Slide 26: Numerical Validation (Cont’d)
A, and 30% AV market penetration, Group 1 recruits steadily decline, while Group 2 recruits steadily rise as the smoothing effect increases
Scenarios |  | Smoothing effect |  | 
 |  | Marginal increasing | Linear | Marginal decreasing
Cost of agency | Uniform | (a) | (b) | (c)
 | Truncated normal | (d) | (e) | (f)

## Slide 27: Second-Best Solution
A, , , and 30% AV market penetration, both groups see higher recruitment and incentives as the budget increases
Scenarios |  | Smoothing effect |  | 
 |  | Marginal increasing | Linear | Marginal decreasing
Cost of agency | Uniform | (a) | (b) | (c)
 | Truncated normal | (d) | (e) | (f)

## Slide 28: Controlling CAVs for Network Efficiency

## Slide 29: Problem Setting
We consider a general network where the routes or/and departure times of a fraction of CAVs can be controlled to reduce cumulative system travel cost over time.
Mike Smith
(2007 INFORMS
Robert Herman Lifetime Achievement Awardee)
Uncontrolled vehicles (UVs) behave selfishly, adjusting their choices day-to-day following a certain dynamics like the one proposed by Smith (1984), though this process is not necessarily known to the traffic authority.
We thus aim for a model-free, distributed control policy that lets CAVs act based on local information.

## Slide 30: Finite-Agent Optimal Control Problem
If the transition kernels and , as well as the system cost are Lipschitz continuous w.r.t and , there always exists an optimal policy
Proposition
Finding such a policy becomes intractable as the number of agents grows large*
*Yang, Y., R. Luo, M. Li, M. Zhou, W. Zhang, and J. Wang (2018) Mean field multi-agent reinforcement learning. Proceedings of the 35th International Conference on Machine Learning, PMLR 80:5571-5580.
  Transition kernel for uncontrolled vehicles
  Sample action from CAV routing policy
  Transition kernel for CAVs
  Total discounted cost over time
Notes: human driver’s response
Assign travel choice for each CAV
Each CAV’s response to the assignment

## Slide 31: Mean-Field Approximation
Let
CAVs (modeled by a Markov decision process)
State (current travel choice), a realization of a random variable whose distribution matches the MF distribution
Action (choosing next travel choice) sample from policy
Transition
Uncontrolled vehicles (UV) (modeled by a Markov process)
State: the empirical distribution , a mean-field travel choice distribution under the law of large numbers
Transition
as the state (population state) population cost (system travel cost)
Let , and represent the state-action joint distribution across the CAVs as the population action (CAV assignments)
The action is sampled from a new policy
Transition (population response)
where

## Slide 32: Mean-Field Approximation
 | Finite Agent Control | Mean-Field Control
State | Current route choice of each CAV Route choice distribution of UVs | Current route choice distributions of two groups (representative agents)
Action | Assigned route choice of each CAV | Joint distribution of current and assigned route choices for all CAVs (population action)
Transition | Each CAV follows assignment UVs follow day-to-day dynamics | CAVs follow a population kernel UVs follow day-to-day dynamics
Cost | Total cost of all vehicles | Total cost of all vehicles

## Slide 33: Single-Agent Mean-Field Control
If the transition kernels and , as well as the system cost are Lipschitz continuous w.r.t and , there always exists an optimal policy for MFC
Proposition*
*Cui, K., C. Fabian, Tahir, A., and H. Koeppl (2024) Major-Minor Mean Field Multi-Agent Reinforcement Learning, Proceedings of the 41st International Conference on Machine Learning, PMLR 235:9603-9632.
  Transition kernel for uncontrolled vehicles
  Sample action from the population policy
  Transition kernel for CAVs

## Slide 34: RL-Based Distributed Policy *
Input: Initialize population policy |  | 
for iterations do |  | 
 | Sample population action Broadcast | 
 | for CAV agent do | 
 |  | Retrieve individual policy from Sample and execute action
 | end for | 
 | Observe cost , next population state | 
 | Update policy (with RL algorithms) | 
end for |  | 
 | end for | 
end for |  | 
*Wu, M., Wang, M., Yin, Y. and Lynch, J. (2024) Leveraging connected and automated vehicles for participatory traffic control. Transportation Research Part C, Vol. 166, 104757.

## Slide 35: Numerical Experiments
Distributed departure-time policy with Vickrey’s bottleneck setting

## Slide 36: Numerical Experiments (Cont’d)
Implementation of the resulting policy: 100% controllable, random initialization, average of three trials
Notes: In the experiment, the departure rate on day 0 is randomly generated, and the rate on all following days is induced by the trained policy. I plotted the average curve of 20 experiments for the first three days, as well as the theoretical SO curv

## Slide 37: Concluding Remarks

## Slide 38: Key Takeaways
Advancements in connectivity and automation will make travelers more willing to give up personal control over their travel choices.
CAVs with relinquished agency can serve as “traffic demand distributors,” coordinating routes and departure times to enhance system performance.
Controlling ~15–20% of traffic can be effective, but required share varies by context.
Incentives help recruit CAVs by compensating drivers for their reduced control and any added travel costs.
Implementing such schemes is likely economically sensible for managing rush hour congestion in large cities.
Mean-field reinforcement learning effectively trains distributed control policies.
Participatory traffic control could be a promising addition to our congestion management toolbox.

## Slide 39: Synergistic Integration with Other Instruments*
  For example, participatory traffic control, when integrated with path-based pricing, can create synergies that offset each method’s weaknesses.
Network | Zones | Nodes | Links | MCR (%) | Zero –Revenue MCR (%)
Anaheim | 38 | 416 | 914 | 21 | 0.73
Barcelona | 110 | 1020 | 2522 | 36 | 0.32
Berlin-Mitte-Prenzlauer Berg-Friedrichshain-Center | 98 | 975 | 2184 | 14 | 0.06
Eastern-Massachusetts | 74 | 74 | 258 | 20 | 0.48
Sioux Falls | 24 | 24 | 76 | 14 | 0.70
Terrassa | 55 | 1609 | 3264 | 57 | 23
Winnipeg | 147 | 1052 | 2836 | 42 | 0.6
*Chen, Z., Lin, X, Yin, Y. and Li, M. (2020) Path controlling of automated vehicles for system optimum on transportation networks with heterogeneous traffic stream. Transportation Research Part C: Emerging Technologies, 110, 312-329.

## Slide 40: Controlling CAVs to Stabilize System Dynamics*
Leveraging -dissipativity for stabilizing discrete-time mixed-traffic dynamic systems
Dissipation Inequality
Flows
Time
Payoff Dynamics (PDM)
Flows
Payoff
Evolutionary Dynamics (EDM)
Payoff Dynamics (PDM)
Propose novel backward EDM
Prove EDM dissipativity by finding ,
Design controller / payoff mechanism to enforce
CAV Control
Flows
Time
* Lee, R., Scruggs, J., and Yin, Y. (2025) Discrete-Time Stabilization of Nash Equilibrium for Mixed Traffic Routing. 2025 American Control Conference, July 8-10, 2025, Denver, CO, USA

## Slide 41: Evolution of Traffic Control
Level of AV Market Penetration
Level of Relinquished Travel Agency
Traditional traffic control for self-organizing systems
Participatory control for semi-organized systems
Reservation-based control for fully-organized systems

## Slide 42: Email: yafeng@umich.edu
Yafeng Yin, Ph.D.
Donald Cleveland Collegiate Professor of Engineering
Donald Malloure Department Chair of Civil and Environmental Engineering
University of Michigan, Ann Arbor
Thank You

## Slide 43: Numerical Experiments (Cont’d)
Sioux Falls Network
Distributed routing policy:
Notes: The total travel cost in an episode (200 days)
Every episode is randomly initialized:
Penetration rate =0; Randomness due to initialization, Normalize its average to 1,
The lower bound is that the system directly arrives at and maintain SO since the second day